## Slide 1: Distance Vector Multicast Routing Protocol (DVMRP)
Multicast routing protocol, RFC1075 (1988).
Used in first internet multicast backbone (MBONE, 1992).
IPv4 address types: unicast, broadcast, multicast.
Not connection-oriented, best-effort delivery (IP).
Not guarenteed to reach all group members.
Hosts are free to join or leave a group at any time.
Sender need to be aware of group members.
Multicast conserves bandwidth by forcing network to do packet replication.
Radio / VIdeo broadcasts, Video conferencing, Distance learning
Shared applications, Multiplayer gaming, Chat rooms
Advertisements, Stocks, Distributed databases

## Slide 2: Multicast Backbone (MBONE)
Interconnected subnetworks and multicast routers.
Created by Jacobson, Deering, Casner (1992).
Uses tunnels for connecting through unicast routers.
Uses DVMRP, MOSPF for routing along with IGMP.
IP Address: 224.2.0.0 (audio 64kbps, video 120 kbps)
IETF meetings, US House & Senate sessions
NASA Space shuttle missions, Satellite weather photos
1992: 40 subnets in 4 countries
1993: Live band performance by Severe Tire Damage
1995: M-bone links in Russia, Antarctica
1996: 2800 subnets in 25 countries
2008: Virtual video conferencing system in use

## Slide 3: Multicast Addressing
Class D IP addresses are used for multicast.
Start with "1110" followed by 28-bit group ID.
Fixed vs Transient multicast IP (logical address).
224.0.0.0: Reserved Class D
224.0.0.1: All multicast devices
224.0.0.2: All multicast routers
224.0.0.4: All DVMRP routers
224.0.0.5: All OSPF routers
224.0.1.11: IETF-1-Audio
224.0.1.12: IETF-1-Video
224.0.0.255: Last reserved for routing
239.0.0.0: Site-local applications
239.255.255.255: Last Class D

## Slide 4: Distance Vector Routing (eg. RIP)
Find the least cost path between 2 nodes.
Also called Bellman-Ford algorithm (distributed).
Each node maintains a routing table.
Originally used in ARPAnet, RIP (now used rarely).
Initial: Distance (cost) to its neighbours is known.
Goal: Distance to all neighbours & next-hop known.
Routing table info is shared with neighbours (except next-hop).
On receiving message, routing table updated with min-cost path.
After N rounds, N+1 hop paths become known.
Triggered update: link / node failure or cost change
Periodic update: Still alive, update DV if some route becomes invalid
Periodic update helps when a route becomes invalid
Bellman-Ford distance update equation

## Slide 5: Multicast Flooding
Router / Host sends packet on all interfaces.
If router has been seen packet before, its discarded.
Used on local network for multicast communication.
Filtering can be done with Multicast MAC address.
Each Host Receives the Multicast Stream
Multicast Stream is filtered by Switch through Multicast MAC address

## Slide 6: Internet Group Management Protocol (IGMP)
Hosts tell router about group membership (RFC 1112).
Router uses this to help route multicast packets.
Filtering can be done with IGMP snooping by switch.
Report: Host says to router, "I want to receive multicast data for X.X.X.X".
Query: Router asks hosts, "Is anone still interested in data for X.X.X.X"?
Report is sent to address X.X.X.X, and received by other members & router.

## Slide 7: Reverse Path Multicasting (RPM)
Forward packet that arrives on shortest path to source.
Router discards packet if it arrives on any other interface.
Delivery tree is truncated if leaf subnet has no members.
Prune message is sent if all child links are truncated.
Opt: Forward only if on downstream router's shortest path.
Duplicates are possible since shortest path is source-based.
RPB
TRPB
RPM
Reverse Path Broadcasting (RPB)
Truncated Reverse Path Broadcasting (TRPB)
Opt. Reverse Path Broadcasting (RPB)
RPB
Reverse Path Multicasting (RPM)
Net3 recieves 2 packets

## Slide 8: DVMRP
It is a distance vector multicast protocol, like RIP.
Suitable for use within autonomous system.
Tunnels are used between non-multicast routers.
Routers need to run a unicast protocol too.
Reverse path multicasting (RPM) used between routers.
Intially (S,G) packet is broadcasted using TRPB.
IGMP is used to find group members in subnets.
Routers send prune message to parent if subnet has no group member.
Routers send graft message to parent if subnet has new group member.
DVMRP, MOSPF, PIM: within Autonomous System
MBGP: between Autonomous Systems
DVMRP Routing table
DVMRP Forwarding table

## Slide 9: DVMRP Datagrams
DVMRP uses IGMP to exchange routing datagrams (type 3).
Message is a stream of tagged data (key=value, … max 512B).
Routers provide periodic and triggered updates.
Messages sent to multicast address 224.0.0.4 (TTL=1).
Request: request route to sources
Response: provide route to sources
Non-membership report: prune path for T seconds (no member)
Non-membership cancellation: graft path (new member)
NULL, Flags0, Infinity, Metric
Address Family Indicator (AFI), Subnet mask
Destination Address (DA)
Requested Destination Address (RDA)
Non Membership Report (NMR)
Non Membership Report Cancel (NMR Cancel)
Commands
Subtypes
NMR for groups 224.2.3.1 & 224.5.4.6 (20s), 224.7.8.5 (40s)
Request all routes (to source).
Response of route for 128.2.251.231 & 128.2.236.2 with metric 2, INF=16, SM=255.255.255.0
Response of route for 128.2.251.231 with metric 2, INF=16, SM=255.255.255.0
DVMRP header

## Slide 10: 406 Submarine Cables
Minimum design life of 25 years.
Satellites account for 0.37% of all U.S. international capacity.
The new MAREA cable is capable of carrying 208 Tbps.
Google, Facebook, Microsoft, and Amazon are major investors in new cable.
Total 1.2 million km (2020)

## Slide 11: Manufacturing & Deployment
Japanese NEC developed 20 fiber pair (40) cable. (2020)
Google announced a cable with 24 pairs of optical fibers.
Bandwidth of 12-pair Dunant is declared at 250 Tbps.
DWDM allows 100 wavelengths over a single fiber.
Largest manufacturers:
Alcatel Submarine Networks (ASN) (France)
TE SubCom (USA)
Nippon Electric Company (NEC) (Japan)
Prysmian (Italy)
Nexans (France)
Hengtong (China)
Zhongtian (China)
Subcom Fiber Optic Cable Kit.
Lightweight (LW)
> 2000m
Special Application (SPA)
900-2000m
Light
Light-Wire Armored (LWA)
Buried
Single Armored (SA)
400-900m
Double Armored (DA)
Beach joint-400m

## Slide 12
1. Extending
2. Dropping
3. Splicing with other side
4. Dropping

## Slide 13
NEC repeaters with four signal amplifiers are located at the OCC factory in Japan.
Alcatel Submarine Networks Optical Repeater
Network architecture
Cable laying
Hydro Jet

## Slide 14
Polynesia submarine cable
Installation ship
Sea plow for Cable burial
Survey ship
Maintenance ship

## Slide 15
SEA-ME-WE 3
The South-East Asia Middle East Western Europe 3.
Length: 39,000km, Capacity: 100G (1999)
Operators: BSNL (92)
CLS: Mumbai (Tata Comm.), Kochi (Tata Comm.) (39)
FEA
The FLAG Europe Asia (Fiber-optic Link Around Globe).
Length: 28,000km, Capacity: 80Gbps (1997)
Operators: Global Cloud Xchange (RCOM) (1)
CLS: Chennai (Tata Comm.) (18)

## Slide 16: I2ICN
The i2 Cable Network.
Length: 3,100km, Capacity: 8.4Tbps (2002)
Operators: Bharti Airtel (2)
CLS: Chennai (Airtel) (2)
SAFE
The South Africa Far East.
Length: 13,500km, Capacity: 130Gbps (2002)
Operators: Tata Comm. (30)
CLS: Cochin (Tata Comm.) (6)

## Slide 17: TIC
The Tata Indicom Cable.
Length: 3,175km, Capacity: 5.1Tbps (2004)
Operators: Tata Comm. (1)
CLS: Chennai (Tata Comm.) (2)
SEA-ME-WE 4
The South East Asia-Middle East-West Europe 4.
Length: 18,800km (4), Capacity: 4.6Tbps (2005)
Operators: Tata Comm., Bharti Infotel (16)
CLS: Mumbai (Airtel), Chennai (Airtel) (17)

## Slide 18: BLCS
The Bharat Lanka Cable System.
Length: 320km, Capacity: 1Tbps (2006)
Operators: BSNL (2)
CLS: Tuticorin (Reliance) (2)
FALCON
The FLAG Alcatel-Lucent Optical Network.
Length: 11,859km, Capacity: 2.56Tbps (2006)
Operators: Global Cloud eXchange (16)
CLS: Mumbai (Reliance) (17)

## Slide 19: SEACOM
The SEACOM Cable.
Length: 17,000km, Capacity: 1.5Tbps (2009)
Operators: (5)
CLS: Mumbai (Tata Comm. / VSNL) (9)
IMEWE
The India Middle-East Western-Europe.
Length: 12,091km, Capacity: 5.6Tbps (2010)
Operators: Bharti Airtel, Tata Comm. (9)
CLS: Mumbai (Tata Comm.) (10)

## Slide 20: EIG
The Europe India Gateway.
Length: 15,000km (4), Capacity: 3.8Tbps (2011)
Operators: Bharti Airtel, BSNL (16)
CLS: Mumbai (Airtel) (12)
TGN-EA
The Tata Global Network-Eurasia.
Length: 9,280km, Capacity: 1.28Tbps (2012)
Operators: Tata Comm. (1) (RTD: 92ms)
CLS: Mumbai (Tata Comm. / VSNL) (5)

## Slide 21: GIBY
The Gulf Bridge International.
Length: ?km, Capacity: 5.6Tbps (2012)
Operators: Bharti Airtel (?)
CLS: Mumbai (Sify Tech.) (10)
MENA
The Middle East North Africa.
Length: 8,800km, Capacity: 5.8Tbps (2014)
Operators: Bharti Airtel (?)
CLS: Mumbai (Sify Tech.) (7)

## Slide 22: CANI
The Chennai - Andaman and Nicobar Islands.
Length: 2300km, Capacity: 6.4Tbps x 4 (Aug 2020)
Operators: BSNL (?), Cost: 1224 Cr.
CLS: (9), Handled by: NEC Corp. (Japan)

## Slide 23: Cable Landing Stations in India
GCX: Reliance Globalcom B.V.
IOX: India Ocean eXchange

## Slide 25: Landing of an Italy-USA cable (4,704 nautical miles long), on the Rockoway beach, New-York, January 1925.

## Slide 26: Request For Comments
RFCs cover many aspects of computer networking, including protocols, procedures, programs, and concepts, as well as meeting notes, opinions, and sometimes humor.
RFCs area associated with an active IETF Working Group.
Published RFCs never change. Technical & Editorial Errata are provided.
Started 7 Apr 1969, by Steve Crocker
RFC 1: Host Software
RFC 2555: 30 Years of RFCs
https://ietf.org/standards/rfcs/
www.arkko.com/tools/rfcstats/

## Slide 27: IETF Working Groups
Applications & Real-Time area (29)
General area (2)
Internet area (17)
Operations & Management area (14)
Routing area (24)
Secutiry area (25)
Transport area (11)
https://ietf.org/standards/rfcs/
https://datatracker.ietf.org/wg/
www.arkko.com/tools/rfcstats/

## Slide 28: April RFCs
RFC527: ARPAWOCKY (1973)
Beware the ARPANET, my son;
The bits that byte, the heads that scratch;
Beware the NCP, and shun
the frumious system patch,
RFC7511: Scenic Routing for IPv6 (2015)
This document specifies a new routing scheme for the current version of the Internet Protocol version 6 (IPv6) in the spirit of "Green IT", whereby packets will be routed to get as much fresh-air time as possible.
RFC2549: IP over Avian Carriers with Quality of Service (1999)
The following quality of service levels are available: Concorde, First, Business, and Coach. Concorde class offers expedited data delivery. One major benefit to using Avian Carriers is that this is the only networking technology that earns frequent flyer miles, plus the Concorde and First classes of service earn 50% bonus miles per packet. Ostriches are an alternate carrier that have much greater bulk transfer capability but provide slower delivery, and require the use of bridges between domains.
IPoAC: IP over Avian Carriers
RFC 3514 The Security Flag in the IPv4 Header 1 April 2003 The bit field is laid out as follows: 0 +-+ |E| +-+ Currently-assigned values are defined as follows: 0x0 If the bit is set to 0, the packet has no evil intent. Hosts, network elements, etc., SHOULD assume that the packet is harmless, and SHOULD NOT take any defensive measures. (We note that this part of the spec is already implemented by many common desktop operating systems.) 0x1 If the bit is set to 1, the packet has evil intent. Secure systems SHOULD try to defend themselves against such packets. Insecure systems MAY chose to crash, be penetrated, etc.

## Slide 29: Regional Internet Registries (RIRs)
(InterNIC, 1996)
RFC2050 (1996)
(1996)
(1996)
(2002)
(2005)
Coordinating body for 5 RIRs
Each RIR received its last /8 IPv4 address block from IANA on 3 February 2011
A Regional Internet Registry (RIR) manages the allocation and registration of Internet number resources in a particular region of the world and maintains a unique registry of all IP numbers issued.

## Slide 30: National Internet Registries (RIRs)

## Slide 35
M: 0 ASN: 0 IPv4: 405 IPv6: 0 S: 1
M: 27 ASN: 1 IPv4: 513 IPv6: 0 S: 2
M: 55 ASN: 47 IPv4: 993 IPv6: 0 S: 3
M: 114 ASN: 63 IPv4: 1050 IPv6: 0 S: 5

## Slide 36
M: 200 ASN: 98 IPv4: 274 IPv6: 0 S: 5
M: 249 ASN: 108 IPv4: 166 IPv6: 0 S: 6
M: 396 ASN: 128 IPv4: 232 IPv6: 5 S: 12
M: 602 ASN: 230 IPv4: 353 IPv6: 14 S: 23

## Slide 37
M: 699 ASN: 220 IPv4: 360 IPv6: 25 S: 31
M: 767 ASN: 203 IPv4: 301 IPv6: 86 S: 33
M: 879 ASN: 198 IPv4: 422 IPv6: 50 S: 40
M: 978 ASN: 186 IPv4: 568 IPv6: 57 S: 44

## Slide 38
M: 1157 ASN: 245 IPv4: 705 IPv6: 51 S: 46
M: 1362 ASN: 298 IPv4: 864 IPv6: 42 S: 46
M: 1584 ASN: 308 IPv4: 917 IPv6: 63 S: 57
M: 1855 ASN: 418 IPv4: 984 IPv6: 160 S: 62

## Slide 39
M: 2170 ASN: 436 IPv4: 1065 IPv6: 185 S: 63
M: 2521 ASN: 505 IPv4: 1358 IPv6: 643 S: 65
M: 2947 ASN: 495 IPv4: 1475 IPv6: 620 S: 70
M: 3534 ASN: 581 IPv4: 1075 IPv6: 562 S: 71
Each RIR received its last /8 IPv4 address block from IANA on 3 February 2011

## Slide 40
M: 3779 ASN: 306 IPv4: 744 IPv6: 255 S: 68
M: 4051 ASN: 646 IPv4: 3914 IPv6: 484 S: 70
M: 5268 ASN: 881 IPv4: 4498 IPv6: 785 S: 76
M: 5994 ASN: 881 IPv4: 4498 IPv6: 785 S: 75

## Slide 41
M: 6557 ASN: 1226 IPv4: 2235 IPv6: 1377 S: 77
M: 7162 ASN: 912 IPv4: 2199 IPv6: 1430 S: 80
M: 7776 ASN: 1560 IPv4: 2027 IPv6: 1472 S: 77
IPv6 adoption increased, with the proportion of Members holding IPv6 resources reaching 61% and total IPv6 capability reaching 22%