## Slide 1: 406 Submarine Cables
Minimum design life of 25 years.
Satellites account for 0.37% of all U.S. international capacity.
The new MAREA cable is capable of carrying 208 Tbps.
Google, Facebook, Microsoft, and Amazon are major investors in new cable.
Total 1.2 million km (2020)

## Slide 2: Manufacturing & Deployment
Japanese NEC developed 20 fiber pair (40) cable. (2020)
Google announced a cable with 24 pairs of optical fibers.
Bandwidth of 12-pair Dunant is declared at 250 Tbps.
DWDM allows 100 wavelengths over a single fiber.
Largest manufacturers:
Alcatel Submarine Networks (ASN) (France)
TE SubCom (USA)
Nippon Electric Company (NEC) (Japan)
Prysmian (Italy)
Nexans (France)
Hengtong (China)
Zhongtian (China)
Subcom Fiber Optic Cable Kit.
Lightweight (LW)
> 2000m
Special Application (SPA)
900-2000m
Light
Light-Wire Armored (LWA)
Buried
Single Armored (SA)
400-900m
Double Armored (DA)
Beach joint-400m

## Slide 3
1. Extending
2. Dropping
3. Splicing with other side
4. Dropping

## Slide 4
NEC repeaters with four signal amplifiers are located at the OCC factory in Japan.
Alcatel Submarine Networks Optical Repeater
Network architecture
Cable laying
Hydro Jet

## Slide 5
Polynesia submarine cable
Installation ship
Sea plow for Cable burial
Survey ship
Maintenance ship

## Slide 6
SEA-ME-WE 3
The South-East Asia Middle East Western Europe 3.
Length: 39,000km, Capacity: 100G (1999)
Operators: BSNL (92)
CLS: Mumbai (Tata Comm.), Kochi (Tata Comm.) (39)
FEA
The FLAG Europe Asia (Fiber-optic Link Around Globe).
Length: 28,000km, Capacity: 80Gbps (1997)
Operators: Global Cloud Xchange (RCOM) (1)
CLS: Chennai (Tata Comm.) (18)

## Slide 7: I2ICN
The i2 Cable Network.
Length: 3,100km, Capacity: 8.4Tbps (2002)
Operators: Bharti Airtel (2)
CLS: Chennai (Airtel) (2)
SAFE
The South Africa Far East.
Length: 13,500km, Capacity: 130Gbps (2002)
Operators: Tata Comm. (30)
CLS: Cochin (Tata Comm.) (6)

## Slide 8: TIC
The Tata Indicom Cable.
Length: 3,175km, Capacity: 5.1Tbps (2004)
Operators: Tata Comm. (1)
CLS: Chennai (Tata Comm.) (2)
SEA-ME-WE 4
The South East Asia-Middle East-West Europe 4.
Length: 18,800km (4), Capacity: 4.6Tbps (2005)
Operators: Tata Comm., Bharti Infotel (16)
CLS: Mumbai (Airtel), Chennai (Airtel) (17)

## Slide 9: BLCS
The Bharat Lanka Cable System.
Length: 320km, Capacity: 1Tbps (2006)
Operators: BSNL (2)
CLS: Tuticorin (Reliance) (2)
FALCON
The FLAG Alcatel-Lucent Optical Network.
Length: 11,859km, Capacity: 2.56Tbps (2006)
Operators: Global Cloud eXchange (16)
CLS: Mumbai (Reliance) (17)

## Slide 10: SEACOM
The SEACOM Cable.
Length: 17,000km, Capacity: 1.5Tbps (2009)
Operators: (5)
CLS: Mumbai (Tata Comm. / VSNL) (9)
IMEWE
The India Middle-East Western-Europe.
Length: 12,091km, Capacity: 5.6Tbps (2010)
Operators: Bharti Airtel, Tata Comm. (9)
CLS: Mumbai (Tata Comm.) (10)

## Slide 11: EIG
The Europe India Gateway.
Length: 15,000km (4), Capacity: 3.8Tbps (2011)
Operators: Bharti Airtel, BSNL (16)
CLS: Mumbai (Airtel) (12)
TGN-EA
The Tata Global Network-Eurasia.
Length: 9,280km, Capacity: 1.28Tbps (2012)
Operators: Tata Comm. (1) (RTD: 92ms)
CLS: Mumbai (Tata Comm. / VSNL) (5)

## Slide 12: GIBY
The Gulf Bridge International.
Length: ?km, Capacity: 5.6Tbps (2012)
Operators: Bharti Airtel (?)
CLS: Mumbai (Sify Tech.) (10)
MENA
The Middle East North Africa.
Length: 8,800km, Capacity: 5.8Tbps (2014)
Operators: Bharti Airtel (?)
CLS: Mumbai (Sify Tech.) (7)

## Slide 13: CANI
The Chennai - Andaman and Nicobar Islands.
Length: 2300km, Capacity: 6.4Tbps x 4 (Aug 2020)
Operators: BSNL (?), Cost: 1224 Cr.
CLS: (9), Handled by: NEC Corp. (Japan)

## Slide 14: Cable Landing Stations in India
GCX: Reliance Globalcom B.V.
IOX: India Ocean eXchange

## Slide 16: Landing of an Italy-USA cable (4,704 nautical miles long), on the Rockoway beach, New-York, January 1925.